## Slide 1
1. JOP is downloaded via a FPGA download cable (e.g., ByteBlaster on the PCs parallel port). After FPGA configuration the processor automatically starts and listens to the second channel (the serial line) for the software download.
2. Java application download: the compiled and linked application is downloaded usually
via a serial line. JOP stores the application in the main memory and starts execution at main() after the download.

## Slide 2: Downloading Application
When the FPGA is configured the Java application has to be downloaded into the main memory. This download is performed in microcode as part of the JVM startup sequence. The application is a .jop file generated by JOPizer.
At the moment there are three options:
  Serial line JOP listens to the serial line and the data is written into the main memory. A simple echo protocol performs the flow control. The baud rate is usually 115 kBaud.
  USB Similar to the serial line version, JOP listens to the parallel interface of the FTDI FT2232 USB chip. The FT2232 performs the flow control at the USB level and the echo protocol is omitted.
  Flash For stand alone applications the Java program is copied from the Flash (relative Flash address 0, mapped Flash address is 0x800002) to the main memory (usually a 32-bit SRAM).

## Slide 3: Configuring FPGA
The FPGA is configured via a download cable (with JTAG commands) using within the IDEs or with command line tools such as quartus pgm or jbi32.
For the device to boot automatically, the configuration has to be stored in non volatile
memory such as Flash. Serial Flash is directly supported by an FPGA to boot on power up.
Another method is to use a standard parallel Flash to store the configuration and additional data (e.g. the Java application). A small PLD reads the configuration data from the Flash and shifts it into the FPGA. This method is used on the Cyclone and ACEX boards.

## Slide 4: Static fields
There can be times when it's useful to have values that are shared across all instances of a particular class. Static fields and static constants enable this to happen by belonging to the class and not to the actual objects.

## Slide 5
14915,//length of the application in words
8539,//pointer to special pointers
13538,// pointer to boot method struct: com.jopdesign.sys.Startup:boot()V
10991,// pointer to first non Object method struct of class JVM
13774,// pointer to first non Object method struct of of class JVMHelp
14789,// pointer to main method struct
185,// pointer to static reference fields
37,// number of static reference fields
14,//number of methods
10436,//java.lang.System
13743,//com.jopdesign.sys.RetryException
12136,//java.lang.Integer
10286,//java.lang.Long
11628,//util.Dbg
12914,//com.jopdesign.sys.Cordic
12375,//java.lang.Number
12591,//aspgalsjop.Ctrlcode
13960,//java.lang.StringBuffer
11670,//java.lang.VMFloat
13584,//com.jopdesign.sys.Startup
10511,//com.jopdesign.io.IOFactory
12046,//com.jopdesign.sys.RtThreadImpl
14081,//com.jopdesign.sys.Scheduler
2: static fields of all classes
185: static reference fields of all classes
10036: util.DbgUdp class info
10041: util.DbgUdp method table
10092: util.DbgUdp constants
10698: util.Dbg constants
222: code starts here
//13538: com.jopdesign.sys.Startup.boot()V
//code start: 5841
//code length: 33
//cp: 13587
//locals: 2 args size: 0
5981217,
13913152,
//5841: boot()V
51415250, // 3 16 136 210
277271450, // 16 134 211 154
...
//8560 "mark/reset not suppo..."
8564,//String handle points to the first field
14161,// pointer to String mtab
8565,//char[] handle points to the first element
24,// array length in the handle
8562,//char ref. points to char[] handle
109, 97, 114, 107, 47, 114, 101, 115, ...
8560: String tables

## Slide 6: Class structure
10036: util.DbgUdp class info
10041: util.DbgUdp method table
10092: util.DbgUdp constants
10698: util.Dbg constants
3,//instance size
2,//pointer to static primitive fields
1,//instance GC info
10642,//pointer to super class - util.Dbg
0,//pointer to interface table
10041: util.DbgUdp.<init>()V
//code start: 222
//code length: 6
//cp: 10092
//locals: 1 args size: 1
227334,
10334209,
2,//const pool length
10647,//static, special or private util.Dbg.<init>()V
19,//const pool length
14811,//static, special or private java.lang.Object.<init>()V
10036, //Class: util.DbgUdp
10041, //static, special or private util.DbgUdp.<init>()V
11575,//Class: util.DbgSerial
11580, //static, special or private util.DbgSerial.<init>()V
11630, //static, special or private util.DbgSerial.<init>(Z)V
4609, //virtual index: 9 args: 2 util.Dbg.dbgWr(I)V
5122, //virtual index: 10 args: 3 util.Dbg.dbgReadBuffer([II)I
11616, //static, special or private util.Dbg.wr(Ljava/lang/String;)V
11622,//static, special or private util.Dbg.intVal(I)V
8620, //String: "\r\n"
15360,//virtual index: 30 args: 1 java.lang.String.length()I
8705,//virtual index: 17 args: 2 java.lang.String.charAt(I)C
11608,//static, special or private util.Dbg.wr(I)V
20480,//virtual index: 40 args: 1 java.lang.StringBuffer.length()I
11777,//virtual index: 23 args: 2 java.lang.StringBuffer.charAt(I)C
8627,//String: "true "
8637,//String: "false "

## Slide 7: Store Immediate Instruction
The value to be stored is provided as immediate operand. The memory address is in the register.
Strind:
Rdrf
ldrzt
Ldt
ldrxt
ldt
Wrdm
nop
Pop
Pop
Nop nxt
Strimm:
Nop opd
Rdrf
Strzt
Ldt
ldctrlopdt
ldt
Wrdm
nop
Pop
Pop
Nop nxt
Strdir:
Nop opd
Rdrf
ldctrlopdt
Ldt
ldrxt
ldt
Wrdm
nop
Pop
Pop
Nop nxt

## Slide 8: Program flow
Configure FPGA
Start microcode execution from address 0
Load Java Application from flash or pc
Invoke startup.boot()
1. Send a greeting message to stdout
2. Detect the size of the main memory
3. Initialize the data structures for the garbage collector
4. Initialize java.lang.System
5. Print out JOP’s version number, detected clock speed, and memory size
6. Invoke the static class initializers in a predefined order
Store address of main & Invoke main
Initialize control memory
start fetching from instruction from control memory store
Execute control code
Calculate address to be invoked, push it on stack and shift control to main
Inovke method & return when finished
Store next pc of main in a register
Store next pc of control in a register

## Slide 9: Datacall
jopsys_datacall:
ldmainptrt
ldt
nop opd
nop
ldctrlopdt
ldt
dup
add
sub
ldjpc
nop
stctrlpc
ldmaint
ldt
stjpc
nop
toggle
nop
nop nxt
Ldpointer to main to TOS
Load methodcall # to TOS and Dulicate
Compute method address to be invoked (sub)
Store nxt pc of control in regsiter
load execution addr of main in PC
Shift control to main

## Slide 10: Application Classes
public class Ctrlcode {
int a;
public static int[] cc = {
0x0000, 0x0000, 0x0000, //nopinstr
0x0500, 0x0011, 0x0501, 0x0012, 0x0502, 0x0023, // ldrimm
0x0503, 0x0034, 0x0504, 0x0045, 0x0505, 0x0056,
0x0200, 0x0001, 0x0201, 0x0002, 0x0202, 0x0003, //strimm
0x0301, 0x0312, 0x0323, 0x0334, 0x0345, 0x0356, // strind
0x0410, 0x0001, 0x0420, 0x0002, 0x0430, 0x0003, //strdir
0x0620, 0x0631, 0x0642, 0x0653, 0x0664, 0x0675, //ldrind
0x0716, 0x0003, 0x0727, 0x0004, 0x0738, 0x0005, //ldrdir
0x0810, 0x0003, // andimm
0x0910, 0x0003, //orimm
0x0A10, 0x0003, //addimm
0x0B10, 0x0003, // subimm
0x0C10, //andind
0x0D10, //orind
0x0E10, //addind
0x0F21,//subind
0x0100, 0x0001, 0x0100, 0x0002, 0x0100, 0x0003, // datacall
0x0100, 0x0004, 0x0100, 0x0000, 0x0000, 0x0000,
};
public int getelement(int a){
return cc[a]; }
}
public class aspgals {
private static void m3(){
System.out.println("Hello World from JOP3!"); }
private static void m2(){
System.out.println("Hello World from JOP2!"); }
private static void m1(){
System.out.println("Hello World from JOP1!"); }
private static void m0(){
System.out.println("Hello World from JOP0!"); }
public static void main(String[] args) {
Ctrlcode code = new Ctrlcode();
int length = code.cc.length;
for (int i=0; i < length; i++) {
int ctrl_instr=code.cc[i];
Native.initctrl(i, ctrl_instr);
}
System.out.println("initialized the control memory!");
while(true) {
Native.exectrl(); // shifts the control to CM
int methaddr=Native.rddatacall(); //read TO
Native.invoke(0, methaddr); //
}
}
}

## Slide 11: Ldr Instruction
The value to be stored is provided as immediate operand. The memory address is in the register.
ldrind:
  Rdrf
  ldrxt
  Ldt
  rddm
  nop
  Pop
  Pop
  Nop nxt
jopsys_ldrimm:
nop opd
nop
ldctrlopdt
ldt
nop
wrrf
nop
pop nxt
Strdir:
  Nop opd
  Rdrf
  ldctrlopdt
  Ldt
  ldrxt
  ldt
  Wrdm
  nop
  Pop
  Pop
  Nop nxt

## Slide 12
Method Cache
Control Memory
Control data Structure
Jump Table
for execution from cache
Jump Table for the Ctrl Code
Microcode
ROM
Register file
RegX
RegZ
T
mainjpc
ctrljpc
mainptr
dmstart
application
Register file
B
A
Heap
Main
Memory Organization